## Slide 1: SHRI VAISHNAV VIDYAPEETH VISHWAVIDYALAYA
(COMPUTER SCIENCE ENGINEERING)-INFORMATION AND CYBER SECURITY
HACK BOX

## Slide 2: HACK BOX
PROJECT REPRESENTATIVE
Siddartha khandelwal
TEAM MEMBERS
Sneha shukla
Somuya sharma
Kartik bajpay
Sumit prajapat

## Slide 3: INTRODUCTION
Those in the security community are most likely familiar with the USB rubber ducky. On the off chance that you haven’t heard of it, the ducky is a device with the form factor of a standard USB drive. However instead of simply storing files, the rubber ducky can emulate a Human Interface Device (HID) such as a keyboard and mouse. It can perform any task you would be able to using these devices, except it can type at the speed of a computer.
This allows an attacker to plug in the ducky, deliver their payload at lightning speed, and get the hell out.
That being said, the ducky has some limitations. First of all, it is $50 for a single unit, which seems like a lot for a tiny flash drive with a single capability. Secondly, the default language “Duckyscript” does not allow for particularly advanced payloads. Payloads can be selected with physical dip switches on the device.
Then I heard about P4wnP1, which solves many of the issues mentioned above. P4wnP1 runs on a raspberry pi, a tiny but fully featured linux computer. This means that on top of the HID injection features of the rubber ducky, there is a lightweight installation of Kali Linux under the hood, ready for you to use as a malicious AP, pivot box, network sniffer, or whatever else you would do with Kali.

## Slide 4: TECHNICAL DETAILS
Required hardware:
Raspberry pi ZeroW
GPIO pins
OLED display hat
Micro SD card(s)
USB A addon board

## Slide 5: Features
Plug&Play USB device emulation
• USB functions:
o USB Ethernet (RNDIS and CDC ECM)
o USB Serial
o USB Mass Storage (Flashdrive or CD-Rom)
o HID Keyboard
o HID Mouse
• runtime reconfiguration of USB stack (no reboot)
• detection of connect/disconnect makes it possible to keep HACK BOXpowered up (external supply) and trigger action if the emulated USB device is attached to a new host
• no need to deal with different internal ethernet interfaces, as CDC ECM and RNDIS are connected to a virtual bridge
• persistent store and load of configuration templates for USB settings

## Slide 6
HIDScript
• replacement for limited DuckyScript
• sophisticated scripting language to automate keyboard and mouse
• up to 8 HIDScript jobs could run in parallel (keep a job up to jiggle the mouse, while others are started on-demand to do arbitrary mouse and keystroke injection seamlessly)
• HIDScript is based on JavaScript, with common libraries available, which allows more complex scripts (function calls, using Math for mouse calculations etc.)
• keyboard
o based on UTF-8, so there's no limitation to ASCII characters
o could react on feedback from the hosts real keyboard by reading back LED state changes of NUMLOCK, CAPSLOCK and SCROLLLOCK (if the target OS shares LED state across all connected keyboards, which isn't the case for OSX)
o take branching decisions in HIDScript, based on LED feedback
• mouse
o relative movement (fast, but not precise)
o stepped relative movement (slower, but accurate ... moves mouse in 1 DPI steps)
o absolute positioning on Windows (pixel perfect if target's screen dimensions are known)
• Keyboard and mouse are not only controlled by the same scripting language, both could be used in the same script. This allows combining them in order to achieve goals, which couldn't be achieved using only keyboard or mouse.
• current language layouts: br, de, es, fr, gb, it, ru and us

## Slide 7: INNOVATION & USEFULNESS
Rubber ducky
Penetration testing of network and wireless devices

## Slide 8: CURRENT STATUS OF DEVELOPMENT
In prototype 1 stage
Circuit building and gathering of required components